MICRO PROCESSOR

First Developed processors: 4004, 8085, 8086

8088: (PC) Personal Computer:

- System speed (or) CPU speed (or) clock speed (or) processor speed 4.77 MHZ.

- 8 bit internal data bus.

- 8088 chip 40 pin Dual Inline packages (DIP)

- Made up plastic packages with 20 pins on each sides.

- 20 bit address line processor support 1MB memory capacity.

- Co-processor 8087.

- It was developed in1979.

80286:

- Processor speed 6MHZ

- Introduced in 1981

- Two types of Mode (i) Real mode (ii) Protected mode

- Real mode and Protected Mode
Multitasking-support. What happens in one area of memory doesn’t affect other programs. Protected mode supported by Windows 3.0.

- 1GB virtual memory

- co-processor 80287.

- Maximum 16 MB memory support.

- 68 pins

80386:

- 12MHZ speed

- 32 bit Register

- 32 bit data bus

- support 4GB memory support

- real mode, protected mode, Advanced virtual memory 64 TB

- co-processor 80387

- It was developed in 1985.

80386 DX:

- 32 bit internal data bus, 32 bit external data bus, 32 bit register is used.

- 132 pin packages

- speed 16 to 33 MHZ

80386 SL:(SL Low Power):

- This processor has many power management facility such as “sleep mode” etc.

- Speed 25 MHZ

- IBM corp. company manufactured.

- IBM has added a 8KB cache MEMORY in the processor or first development the cache memory.

80486:

- 80486 processor first development math co-processor.

- Microprocessor built in math co-processor.

- Internal cache memory 8KB.

- Internal and external 32 bit data bus.

- Speed range 20 MHZ – 50 MHZ.

- It was developed in1989.

Pentium – I /80586:

  - Intel Company Pentium Name development.

  - This word Pentium comes from the Greek word penta, which means five.

  - It was developed in 1993.

  - Super Scalar Architecture:

  - The ability of the processor to execute two instruction simultaneously is called super scalar architecture by inter.

  - (2 instruction pipelines for execution of up to 2 instructions per clock cycle)

  - Pentium processor math co-processor in built internally.

  - 64 bit math co-processor.

  - 100 MHZ – 200 MHZ speed.

  - Intel company fifth generated processor.

  - Internal 8kB caches for code and data
(but external L2 cache)

  - Addressbus: 32b. External Databus: 64b
But not a 64-bit processor!

Pentium MMX technology:

- Pentium P5 with MMX Extensions

- D-bus: 64b. A-bus: 32b

- 66-266MHz

- L1-caches: 16kB code and data (write-back).

- 321-pin socket 7

- MMX = Multi-media Extensions
To meet growing importance and increasing demands of multi-media and communication applications

- 57 new instructions
New instructions designed specifically to handle video and audio data

- SIMD = Single Instruction Multiple Data
One instruction performs the same function on many pieces of data

Celeron processor:

- Speed 600 MHZ to above 2.40 GHZ

- 100 MHZ multi-transaction processor system bus on Intel Celeron Processor at 800 MHZ and Greater frequencies.

- Includes Intel MMX multimedia Enhancement technology.

Level –I

32 K Bytes (16k byte /16k byte) level 1 cache memory.

Level – II

- 128k byte Integrated Level 2 cache on 600 MHZ to 1.10GHZ.

- 256k byte Integrated level 2 cache on 2.40 GHZ speed.

Pentium II processor:

- Processor core speeds: 233-450MHz

- Bus speeds: 66-100MHz

- MMX

- A-bus: 32b
Addressable: 64GB

- L2 cache
Half core-speed.
Supports up to 512MB

Pentium III:

System Bus frequency

66 MHZ – 100 MHZ – 133 MHZ

32 bit address bus

32 bit data bus.

32KB (16 KB / 16 KB)

Intel mmx media in clued the technology.

It was developed by 1999.

Pentium IV:

- speed 2.66 GHZ, 3.2 GHZ, 3.8 GHZ

- system bus frequency 400 MHZ

- L2=> 256KB, L1=> 32k two type of cache memory.

- 4 GB memory support.

- High speed video signal transfer using to AGP 8x

- It was developed by 2000.

- 32 – 64 bit data bus.

Intel xeon processor:

- High speed processing

- Two processor socket support.

Itanium processor:

- system bus frequency above 733 MHZ to 800 MHZ speed.

- 64 bit data transfer.

- Three types of level cache memory.

- L3=> 2MB (or) 4MB L2=>256KB L1=>32KB

- 16 TB memory support.

AMD processor :( Advanced micro device)

- 1969 starting the company.

- AMD 188, AMD 286, AMD386, AMD 386SX, AMD 486, AMD 486DX, AMD K5, AMD K6, K6-II, K6-III, AMD K7, AMD Atlon, AMD Atlon XP, AMD Duran, AMD Hemar.

PROCESSOR GENERATION

First Generation		:	8086, 8088

Second Generation		:	80286

Third Generation		:	386 DX, SX

Fourth Generation		:	486DX, SX, 386 DX4

Fifth Generation		:	P – I, AMD K5, Cyrix 5X,

P-MMX, AMD K6, Cyrix 6X 86

Sixth Generation		:	P-Pro, P-MMX, Celeron, P – II, P – III, AMD K6-3.

Seventh Generation		:	P – IV, Xeon, AMD Atlon, Atlon XP.

Eighth Generation		:	Intel Itanium, AMD Hemar.